## Slide 1: Agenda:
Introduction to IoT – Azure – Azure IoT Hub
Importance & process of planning
Get started with Azure IoT Hub
IoT Solutions
Managing the devices

## Slide 2: A Simple Thing
Notes: Example Script:
Proliferation
If you’ve been to a mall, through airport security or even a public bathroom lately you may have seen a device like this for quickly giving customer service feedback. These kinds of simple devices are showing up – and sometimes not visibly - more and more and they provide valuable data that in some cases can produce actionable results in real-time
How it works
This device doesn’t require much compute power, and in fact a single button is likely bigger than the control board inside. Such a device can easily collect a large volume of data and with a simple wifi connection, sent the data to a back end for data processing.
Where the data goes
The data may only be stored in local storage, but for real leverage, the data will go live – perhaps with an offline buffer – to a server on premise or in the cloud. Again, not much processing power is necessary to make this happen.
Live results -> actions
What if many people in a row click the angry button? Will this be noticed? Will someone know why this has happened or even could have anticipated it? If the device stops sending data, will some system be automatically checking to see if the device is up and running vs. being the victim of a smash from a big angry-green guy.
Connected insights
Is there is a link between nearby resource levels (perhaps in the number of employees working) and the current stream of results coming from this device? Can we automatically alert the resource manager once the back end system sees a string of negativity or even automatically request and re-allocate additional resources?
A simple thing can become part of a powerful connected thing.

## Slide 3: Connected Things Everywhere
%
NOW
More connected devices than people
2020
> 25 billion (Gartner predicts)
$1.7 trillion market (IDC report)
Notes: Example Script:
Devices increasing
Devices in our world are becoming increasingly connected, and showing up in all aspects of our lives
CLICK – Retail
Stores can now use devices to for example, price check, monitor stock levels, to manage palette deliveries, and keep track of customer activities.
CLICK - Transport/Logistics
Devices on vehicles can monitor tire pressure, ensure refrigerators work, use GPS to capture and relay vehicle position or plug into the vehicle management system to relay a large amount of data that may help manage maintenance.
CLICK – Manufacturing
A manufacturing line can use connected device to ensure the efficiency, ongoing operations and quality of production.
CLICK - Smart buildings/homes
The ability to lower costs, help the environment and feedback into more efficient future designs is changing the future of our cities.
CLICK – Energy
From our national power grid to plug-in energy monitors in our homes, the data collected can improve the economics of supply energy and our understanding of how it’s used in different environments.
CLICK – Healthcare
A fitness band can be considered part of healthcare IoT, in addition to more traditional devices now turning into connected devices in hospitals.
CLICK - Vendor appliances
Grocery stores can use connected refrigerators to help ensure their produce remains fresh. Vending machine suppliers can optimize their deliveries by using connected machines.
CLICK – Mobile
Clearly the mobile phone is one of the most visible connected devices, and we’re seeing more and more personal and wearable connected devices and it’s not about to slow down.
CLICK - More devices than people
There are now more connected devices than people and…
CLICK - 25 billion by 2020
By 2020 Gartner predicts there will be more than 25 billion connected devices.
CLICK - $1.7 trillion by 2020
And by the same year, according to IDC’s report, the IoT market will grow to $1.7 trillion.

## Slide 4: Demo
Be part of the Internet of Things
Notes: 10 min
Let’s show how you can use your browser as a device in the Internet of Things…

## Slide 5: Anatomy of the Internet of Things
Things
I/O
Data
Analysis
Notes: Example script:
CLICK - Things
These are physical things – which may sometimes be simulated in software – that may be business assets, gadgets or perhaps just a sensor with some compute power – maybe a programmable System-on-a-Chip. In essence that are one or more variable characteristics that we can monitor or some function we want to control.
CLICK - I/O
The physical thing needs a connection to the Internet. It may have it’s own TCP/IP stack or need help to make that connection. It could also talk with other attached components like sensors, other devices or with humans. Ultimately, it connects to an endpoint on the Internet.
CLICK - Data
There are various data values being communicated. While a solution within the Internet of Things may collectively capture billions of bytes of data in a short period of time from perhaps millions of sensors, individual things typically only capture and transmit small quantities of data, with the exception that a large batch may be sent when a device comes back on line.
CLICK - Analysis
Analysis of the data can range through various levels of sophistication: a flat list file, an aggregated report, live data monitoring, live aggregation, processing by machine intelligence, or in combination with other available data to present important conclusions. Ultimately the point of analysis is to be able to make actionable decisions.

## Slide 6: Strategic Importance
New data and real-time insights & analysis can lead to competitive advantage through:
  Quick reactions to issues and success
  Increased efficiency
  New opportunities from discovering trends
  Improved customer service
Notes: CLICK – READ
New data and real-time insights & analysis can lead to competitive advantage through:
CLICK – Quick reactions
Having additional data about your systems and optionally performing some analysis can help you react to issues as quickly as possible. Combining the current stream of data in the context of historical data may allow you to predict potentially imminent issues. This could apply to customer interactions in retail, items on a production line, traffic or many other scenarios. Where you see things go well, you can work on discovering the contributing factors and amplify that.
CLICK – Increased efficiency
By gathering data and aggregating it, you may be able to discover areas for improvement. This in turn may lead to lower costs and increased profits.
CLICK – New opportunities
The data you collect may reveal key success factors or a trending behavior which may be unseen to your competitors
CLICK – Improved customer services
Having more data available from the lives of your customers, e.g. location or feedback, or from the components of the service you are offering, e.g. stock levels, may enable you to provide a more informative, detailed or personalized approach.

## Slide 7: Industry Usage
%
Jabil – electronics production line. 1 million data points to anticipate and avert failures in early steps.
Ford – vehicle status.
Added over-air updates, tire/fuel/battery status data, vehicle tracking & remote-start.
Kroger – check-out staffing.
Sensors count customer and are used to monitor and anticipate checkout staffing needs.
Rockwell Automation – oil/gas supply chain.
Connected drilling pumps, transfer units and liquid natural gas bumps give preventative view to stakeholders
ThyssenKrupp Elevator – cloud-connected elevators.
Elevators in major cities enable pre-emptive maintenance.
Weka Health Solutions – portable vaccine fridge
Remote monitoring of temperature and dispensing quantities.
Notes: Let’s look at examples of how IoT is being used in various industries
CLICK - Jabil - Manufacturing
Jabil is a provider of manufacturing, design engineering, and supply chain management technologies and services.
They used an IoT solution to increase the throughput of products while simultaneously decreasing the need for human touch.
They connected an electronics manufacturing production line to the cloud, using it to collect more than 1 million data points from each assembly across a 32-step, four-hour manufacturing process. This enabled them to anticipate and avert more than half of circuit board failures at the second step in the process, and the remaining 45 percent at step 6. The end results are a reduction in scrapped materials and warranty costs, and an increase in customer satisfaction.
CLICK - Ford – Transport
Ford unveiled their Service Delivery Network to deliver over the air updates for vehicle performance, previously done via USB. The network also allows owners to keep tab on their vehicles and the status of components like tires, fuel level, and battery, while providing remote start options. Owners have timely information and Ford gains insights into owner usage.
CLICK – Kroger – Retail
Kroger has reduced its average check-out line wait time from 4 minutes to 26 seconds. They added infrared sensors to count customers so they can monitor and anticipate checkout staffing needs. Transactions and sales both immediately rose.
CLICK – Rockwell Automation – Energy
Rockwell Automation is using IoT to track equipment performance in real-time, predict failures, and help with future designs.
Oil drilling pumps are constantly monitored to help prevent expensive production stalls costing $100,000s.
Product transfer units are monitored and enabled for remote service and maintenance, monitoring for correct product transfer
Liquid natural gas pumps are being installed to deliver this alternative fuel for delivery trucks, and are cloud-connected for monitoring.
Stakeholders across the entire supply line gain useful insights.
CLICK – ThyssenKrupp Elevator – Smart buildings
ThyssenKrupp Elevator installed elevators in the new One World Trade Center building in New York, the CMA Tower in Saudi Arabia, and Bayshore Hotel in Dalian, China. New elevators are cloud connected to go beyond preventative maintenance to pre-emptive maintenance based on the data captured, offering higher uptime.
CLICK – Weka Health Solutions – Healthcare
Weka Health Solutions has a small and portable smart fridge with remote monitoring of vaccine storage temperature and dispensing quantities. Shortages and storage issues can be remotely tracked, predicted and alerted.

## Slide 8: Problems Solved by IoT Solutions
Uncollected data
Dispersed collection
Mass raw data
Lack of live data
Reactionary approach
Preventative maintenance costs
Lack of remote control
Notes: Considering those kinds of industry solutions, we can generalize problems that can be solved by an Internet of Things solution
CLICK - Uncollected data
Organizations may have measurable physical properties throughout their operations which if collected may provide a source of increased efficiencies and commercial competitive advantage. For example, it could be the flow of people, assets or goods or perhaps physical measurements such as temperature, pressure, light or position. Having this data could improve operations and profits.
CLICK - Dispersed collection
Once useful data is identified for collection, those points may be available at physically dispersed locations (for example. different retail location, or equipment across a factory floor), and needs to be brought to a reliable central location for storage and processing.
CLICK - Mass raw data
With so much data coming in, it can be difficult to see problems arising, discover common factors or spot trends.
Once data is collected, it needs to be aggregated, grouped or clustered in a meaningful way.
CLICK - Lack of live data
In many industries, having live data can be critical to minimizing down time or providing a satisfactory response to issues.
CLICK - Reactionary approach
Reactionary responses typically occur when part of a system has failed. The parts and labour needed to effect a repair may be expensive and there may also be a cost (e.g. loss of revenue) for downtime incurred until the situation is remedied. Looking at data over time may lead to a plan for routine preventative maintenance.
CLICK - Preventative maintenance costs
While regular preventative maintenance may help prevent failures, perhaps arranged according to an examined or published mean time between failures, it’s not exact and incurs a regular cost. If a solution is able to alert an organization to impending issues based on incoming data, or otherwise predict an imminent failure before it occurs, there are costs savings to be had,
CLICK - Lack of remote control
Even with these problems solved, it may become apparent that an asset or piece of equipment needs to be adjusted. Sending out a technician or other operative can be costly. Also if data collected or other findings lead to the need to update the firmware of some equipment, it could also be expensive to achieve an update without local human intervention.

## Slide 9: Solution Feature Requirements
Data collection
Device registration
Data upload
Mass data storage
Data routing
(Live) analysis
Reporting
Device management/control
Notes: So now this leads us to the common features of an IoT solution
CLICK - Data collection
We need the ability to first locally collect data from humans or sensors using appropriate devices.
CLICK - Device registration
It must be possible to add devices to the solution and there may be millions of such devices. There will likely need to be a registration process whereby each device has a configured identity and the solution is set to accept data from the device with the new identity.
CLICK - Data upload
A registered device must be able to upload the data it collects. This may happen continuously or in batches. It’s possible that data from multiple devices may be uploaded through a gateway or proxy device.
CLICK - Mass data storage
Given the large amount of data that may be collected, either over time or in a short space of time from many devices, a solution will need to be able to store or at least buffer an appropriate amount of incoming data.
CLICK - Data routing
As data is processed, perhaps aggregated or filtered, it is necessary to decide where the data should be stored or processed next. For example, data from a device, could be generally collected data, or it could be the response to a specific query send to the device.
CLICK - (Live) analysis
Collected data may be processed to transform it, aggregate or roll it up, or compare it against specific patterns. This kind of analysis may happen on historical data or continuously on a window of live data.
CLICK - Reporting
Once the data is suitably processed, it needs to be reported for human consumption as displayable data or specific notifications, or perhaps formatted for use by another system.
CLICK - Device management/control
There’s usually an interface to do things like see the reported data, send commands to one or more devices (including specific actions to upgrade firmware) or to remove devices.

## Slide 10: High-Level Components
%
Cloud Gateway
Analytics, Storage & Routing
UI
LOB Connectivity
Notes: To support those features at the high level we need the following broad components
CLICK – Devices/Things
So we start with a set of devices or things which may be incredibly diverse. We’ll talk in more detail about this shortly.
CLICK – Cloud Gateway
From there we move to the cloud where we need a gateway that can receive messages from devices and provide a way to get messages back to the devices.
CLICK – Analytics, Storage & Routing
We then come to the core analytics, storage and processing. Here we perform aggregation on the incoming data, store data and results and then decide how the data will be routed for further use.
CLICK – UI
Most likely we’ll have a user interface through which we can manage device registration, view data, send commands to devices, see rolled-up views and the results of analyzing the data.
CLICK – LOB Connectivity
Based on the pattern of behavior observed there’s further value in connecting to a broad range of line of business systems, perhaps e-commerce, inventory management, resource management, etc.

## Slide 11: Devices - OS & Languages
%
C
C++
C#
Node.js
Java
Objective C
Swift
Notes: CLICK - Devices
As we’ve seen with the web browser case many things can be a device, or perhaps the IoT device is a sub-system of, or attachment to a device. Devices may be placed in a variety of locations therefore having a variety of potential size, weight and environmental constraints.
CLICK – Operating Systems
Perhaps as a result of placement constraints, or because of organizational or vendor knowledge, a specific operating system may be chosen for the device. A solution therefore needs to find a way to provide the same feature or capabilities across that range of operating systems. It’s possible that a device does not have any of these operating systems, but perhaps a very low-level SoC with limited processing. Such a device would still need some form of communication, though it may not be full-blown TCP/IP.
CLICK – Languages
On any given operating system, there may be a choice of framework or languages and we need to be able to support as many of these as possible. Having SDKs for these development platforms is extremely important to enable a range of skillsets to be able to participate in IoT.

## Slide 12: Desirable Traits of an IoT Cloud Platform
Security
Availability
Maintenance
Support for low-power devices
Support for key messaging formats
Scale
Additive
Templates & Building Blocks
Cloud Gateway
Analytics, Storage & Processing
Presentation
LOB Connectivity
Notes: Turning to the part of the solution that runs in the cloud, the underlying platform needs to provide key traits.
Security
Security is an important aspect of IoT. As well as physically securing the devices, the data in transit and at rest needs the highest possible level of protection. Establishing identity is equally important so we can be sure that the correct data only comes from registered devices and know exactly which devices is sending the data – we don’t want data being attributed to the wrong device.
Availability
The cloud platform may need a high degree of availability and reliability, at least in terms of being available to receive and store messages with minimal data loss. Ideally any data store used, possesses the standard database attributes of Atomicity, Concurrency, Isolation & Durability.
Maintenance
The cloud platform should keep records of the level of functionality available on each device and ideally have the remote ability to update the application code, and perhaps firmware code running on devices connected to the cloud.
Support for low-power & legacy devices
Not every device or thing will have TCP/IP connectivity. For example a tiny system-on-chip device may be able to read basic sensor input, but only have Bluetooth or other low-power wireless networking. We need a way to bridge that gap.
Support for key messaging formats
Legacy code or formats may not be readily compatible with the cloud platform. A solution is needed in this case too.
Scale
A platform may need to handle 10s, 100s, 1000s or perhaps millions of devices all sending many messages per second.
Additive
Ideally, the introduction of IoT should be additive, in that it can be added incrementally while complementing and co-operating well with existing systems. The initial introduction should start to reap organizational benefits which may then guide future IoT incorporation.
Templates & Building Blocks
Getting started with a platform can be a learning-curve. Having starting templates upon which to build and flexible building blocks will help move along the implementation.

## Slide 13: Remote Monitoring Components
Device Hub
LOB Integration
Live Analytics
Device Metadata
Event
Pub-Sub
Storage
Control & Reporting UI
%
Event Routing
Jobs
Device Gateway
Notes: Let’s look at the components in a general solution for remote monitoring.
Devices
We start with our devices. Each one needs to communicate with the cloud components.
Device Hub
All devices ultimately connect to this component which must be able to handle large scaling in some scenarios. It knows the bare minimum for each device. It can identify each device and knows how to find the connection to send messages back to individual device.
Device Gateway – field & cloud
For those devices that do not have TCP/IP connectivity or cannot use compatible formats, there are Device Gateways which sit between a device and the Device Hub. An example field-gateway is one that sits on premise with a device and converts Bluetooth to TCP/IP. An example cloud-gateway may be one that translates messaging formats between a device that doesn’t use a compatible message format, and the Device Hub.
Live Analytics
Data is taken from the device hub (and possibly other stores) and rolled-up over a sliding window, examined, and one or more streams of data emerge. Example streams may include: an aggregate of the live data or ‘telemetry’ sent from devices; specific metadata or notifications from a device; the results of a command running on a device or the results of comparing incoming data to alerting rules. This component may need to scale up as more and more data comes in, but can be buffered.
Storage
Live or aggregated data may be stored for historic reporting or for use with other organizational systems. This data in table orientated and design for rapid I/O.
Event Pub-Sub
Certain output stream of the analytics components will form events to be processed further. These events can be published to the Event Pub-Sub component. Multiple other components can then subscribe to perform further tasks.
Event Routing Jobs
Processing events can subscribe to and handle various events to do things like complete a device registration or signal an alert to another system. This component will also help buffer high-demand and can be scaled up if necessary.
along with alerts.
Device Metadata
Data about a device and command interactions with the device are stored here. This is more of a traditional database.
Control & Reporting UI
A web application provides UI to manage and control devices, as well as a dashboard to the show live and historical results, LOB integration
The solution provide hooks to connect to other systems when certain data monitoring rules are met.

## Slide 14: Demo
Walkthrough of a Remote Monitoring Solution
Notes: Demo 1.2 - 10-15 min
Let’s see what the remote monitoring solutions look like in reality.

## Slide 15: Additional Desirable Features
Prediction
Cognition
Notes: Let’s talk about two addition features that can deeply enhance an IoT solution.
Prediction
With a remote monitoring solution we can observe issues almost in real-time. However, it would be better to prevent those issues occurring. One approach is to do preventative maintenance. Based on the known age of field components we may decide to perform regular services. For example, both cars and aircraft undergo regular scheduled maintenance to help avoid issues. However, this is a potentially unnecessary expense in some cases, and may still not prevent earlier-than-anticipated failures. If we can find a relationship between the data from a monitored system and the likelihood of behavior, then we can predict imminent failure or the likelihood of it within a certain window.
Cognition
The data from a device may be coming from or about a human, or taking in data based on the behavior of a human or the objects in the world around us. If the IoT solution is able to be somewhat cognizant of this type of data by deriving machine-understandable values, we can bring semantics to the data which become machine-actionable.

## Slide 16: Predictive Analytics – Machine Learning
Prior Real Data
Training
Algorithm
Trained
Model
Live Real Data
Training
Model
Result
What set of data leads to a certain result?
Will any of this data lead to that result?
Notes: To do predictive analytics we using machine learning to build a trained model.
CLICK
This works be taking real data in which there may be a determinable connection between some portion of the data and a specific part of the data that indicates an outcome of importance, e.g. the data set may include multiple measurements for parts of a refrigeration system as well as a indicator of when the temperature has become unusable. Given a suitable training algorithm, we can constructed a trained model.
CLICK
We can then take live real data, asses it against the training model, and determine a useful prediction such as when the temperature will soon reach an unacceptable level, long before it does. Different models and algorithms may be suited for different patterns of data or different results to be predicted.

## Slide 17: Cognition – Cognitive Services
Vision – recognize objects, moderate content, recognize faces & emotion, and analyze/process video.
Speech – text<->speech, do custom recognition, recognize speakers
Language – spell check, analyze text, understand & analyze language, translate, use web language models
Knowledge – use academic knowledge, explore linked entities, interactively search data, find recommendations
Search – autosuggest, search the web, search for images, news, video
Notes: With a set of cognitive services we can determine and extend upon, machine-readable output in these areas.
Click - Vision – READ LIST
Click – Speech – READ LIST
Click – Language – READ LIST
Click – Knowledge – READ LIST
Click – Search – READ LIST

## Slide 18: Demo
Apply cognitive services to device data
Notes: Demo 1.3 – 10 min
So let’s add some cognitive services to the first demo…

## Slide 19: Resources
Further sessions in this series:
  Starting IoT Solutions – deeper on a remote monitoring solution and connecting devices
  Building Practical IoT Solutions – more on predictive maintenance solution, building a solution and customizing an existing template
Try a solution – http://azureiotsuite.com/
IoT Resources - https://www.microsoft.com/en-us/cloud-platform/internet-of-things

## Slide 20
Author & validation approval – CodeSizzler India Private Limited (MPN)